## Slide 1
“DESIGN AND PRODUCTION WOVEN FABRICS USED IN SURGICAL ROOMS”
SCIENCES &ARTS ,RESEARCHE STUDIES.VOL.20.NO.3 JULY 2008
Ibrahim, G., E.,
Abstract
This research is mainly concerned with designing woven fabrics used in surgical operation rooms (Nurse’s apparel, durable gowns, swabs, towels, drapes, and bedding). The woven technique was applied to produce these fabrics, using cotton yarns. Their influence on the performance of the end-use fabric and the achieved properties were studied. On the other hand physico-chemical properties including; antibacterial, air permeability, water permeability, handle, thickness and weight, were evaluated according to the final product needs
Antibacterial test
Samples were treated with Tinosan cell at concentration 0 %, 5%, 10 % and 15 %, it can be seen from table (2) and figure (1) that there is a direct relationship between Tinosan cell concentrations and antibacterial effect. it could be stated that the efficiency of the antibacterial finish is not affected by the repellent finish, but the effectiveness of the repellent finish varies with the add-on level of The antibacterial finish .
1-we can see from table(1) and figure (2) that untreated fabrics did not provide any resistance against microbes.
2- Treatment of fabrics with Tinosan led to improvement in properties of the anti- microbes.
3- It was found that treatment of the fabrics with cellulose-based substance with Tinosan cell provided good microbe resistance and it increases with the increase in concentration. Concentration of 15% of Tinosan cell has recorded the highest resistance rate against microbe
Results
1-Blanck., H., “Textile in medicine”, International Textile Bulletin ,4th quarter, vol. 41,1995, p.6-8.
2-Mathews,A, and Hardingham, M., “Medical and Hygiene textile production”, Intermediate technology ,Russell press Ltd, Nottingham, UK, 1994,p. 10,15,16,19,20,22,332.
3-Shamash, K, “ A healthy prognosis”, Textile month, December,1980,p.15,16.
4-Megraw,P., “ Textiles may help put medical costs under knife”, Industrial fabric products review, vo.l6, No. 6, October, 1984, p. 28,32.
5-Brody, H., “ Synthetic fiber materials”, Longman groupUK,limited,London,P,1994.,329,334,335
6-Adunur, S., “ Wellington sears handbook of industrial textiles ”, Wellington sear company, Technomic publishing company,Inc.,Lancaster,Pennsylvania,1995,p.6,7,8,133,136,334
7- Ramani, T.,V., and Jacob, M., “ From rag waste to disposable diapers”, The Indian Textile Journal, RS. 30,vol. 100, No. 10, July, 1990, p. 144-145.
References
The experimental Work
This research concerns with producing fabrics suitable for surgical rooms . All samples in the research were produced with cotton yarns using three woven structures ( plain weave 1/1,regular hopsack 3/3 and mock leno) .Three weft sets were also used (22,26 and 30 pick /cm) , using two different yarns counts (30/1 and 40/1 English )
Finishing treatment
In this study, antibacterial finishes was applied to the samples. All samples were treated with Tinosan cell with various concentrations, 0 %, 5 %, 10 % and 15 % concentration. Antibacterial finishes were applied to fabrics to prevent the growth of microorganisms exposed to the fabrics during surgical operations.
Methods and Materials
Introduction
The medical textile section, looked at in its broadest term, is undoubtedly one of the greatest success stories of recent years, The medical and related Hygiene industries have been major users of textiles products for many years. Today there has been a huge increase in both the size of the market and the variety of product available (3) and most industry leaders at all levels of the distributions network, say that there is potential for new products and applications. (4) , and this study aims to produce fabrics used in surgical rooms.
Water permeability ( ml bar ) |  | Weft set | Weft count | Fabric structure
After treatment | Before treatment |  |  | 
2.72 | 5.85 | 22 | 30/1 | Plain weave 1/1
2.5 | 5.5 | 26 |  | 
2.35 | 4.5 | 30 |  | 
2.6 | 3.65 | 22 | 40/1 | 
2.5 | 3.35 | 26 |  | 
2.25 | 3.2 | 30 |  | 
2.0 | 3.6 | 22 | 30/1 | Regular hopsack 3/3
1.75 | 3.3 | 26 |  | 
1.25 | 3.1 | 30 |  | 
1.5 | 3.25 | 22 | 40/1 | 
1.25 | 3.0 | 26 |  | 
1.1 | 2.25 | 30 |  | 
2.6 | 4.0 | 22 | 30/1 | Mock leno
2.3 | 3.5 | 26 |  | 
2.25 | 3.25 | 30 |  | 
2.28 | 3.5 | 22 | 40/1 | 
2.25 | 3.15 | 26 |  | 
2.25 | 3.0 | 30 |  | 
Results of water permeability test applied to produce samples.
( 0) Handle |  | Weft set | Weft count | Fabric structure
After treatment | Before treatment |  |  | 
44 | 41.5 | 22 | 30/1 | Plain weave 1/1
45 | 42.8 | 26 |  | 
45< | 43 | 30 |  | 
43 | 40 | 22 | 40/1 | 
44 | 41.5 | 26 |  | 
45 | 42.5 | 30 |  | 
42 | 40 | 22 | 30/1 | Regular hopsack 3/3
43 | 40.5 | 26 |  | 
44 | 41.3 | 30 |  | 
41 | 39 | 22 | 40/1 | 
42 | 39.6 | 26 |  | 
43 | 39.8 | 30 |  | 
43 | 41.3 | 22 | 30/1 | Mock leno
44 | 42.75 | 26 |  | 
45 | 43 | 30 |  | 
42 | 39.3 | 22 | 40/1 | 
43 | 39.8 | 26 |  | 
44 | 41.8 | 30 |  | 
Results of handle test applied to produced samples